## Slide 1
Evaluating the Use of Satellite Remote Sensing for cyanoHAB Public Health Warnings
NASA CCE Joint Science Workshop
Presenter: Brittany Lopez Barreto1
blopezbarreto@ucmerced.edu
Co-authors: Dr. Erin L. Hestir1, Dr. Christine Lee2, Dr. Marc Beutel1
1University of California, Merced
2NASA JPL Terrestrial Hydrology Group

## Slide 2
Authority | Quantity | Guideline Value Classification | Method
CA DWR | 0.8 - 5.99 µg/L Microcystins | Caution | Field Sampling
 | 6 - 19.99 µg/L Microcystins | Warning | 
 | 20 µg/L ≤ Microcystins | Danger | 
WHO (2021) | Chl-a ≤ 24 µg/L | No Alert | Sentinel-2
 | Chl-a ≥ 24 µg/L | Alert | 
WHO (1999) | ≤ 20,000 cyanobacterial cells/ml or ≤ 10 chl-a µg/L | Low | Sentinel-3
 | 20,000-100,000 cyanobacterial cells/ml or 10.1 - 50 chl-a µg/L | Moderate | 
 | ≥ 100,000 cyanobacterial cells/ml or ≥ 50 chl-a µg/L | High | 
Source: TCiW, Chorus & Testai (2021)
Guideline Values for Cyanobacteria in Recreational Waters
No Alert
Alert

## Slide 3: San Luis Reservoir (SLR)

## Slide 4
Remote Sensing or Field Campaign |  | DWR ​ | 
 | ​ | No Alert​ | Elevated Alert​
 | No Alert​ | Total Agreement​ | Under-predicted Advisory​
Remote Sensing or Field Campaign | Alert​ | Over-predicted Advisory​ | Total Agreement​ ​
Algorithm Matters
Chart: Chlorophyll-a vs Cyanotoxins by CA DWR in San Luis Reservoir
| Lab-based Chl-a | S2 (Gons) | S2 (Moses) | S2 (Mishra) | S3 (CyAN)
Overpredicted Advisory | 0.028571 | 0.25 | 0.53846 | 0.15385 | 0.070423
Underpredicted Advisory | 0.22857 | 0.041667 | 0 | 0.23077 | 0.098592
Total Agreement | 0.74286 | 0.70833 | 0.46154 | 0.61538 | 0.83099

## Slide 5: Final Remarks
SRS can become an important tool in aiding in public health alerts of potential exposure to cyanotoxins
  SRS can measure areas where DWR does not collect samples, and during the times of the year they do not measure
Chl-a products as a proxy for cyanotoxins may work best for the detection of blooms rather than as a measure of their intensity
This study provides a framework for evaluating public health utility of SRS for enhancing cyanotoxin monitoring globally
Notes: Chla products as a product
We used SLR as a
Mention poster,

## Slide 6
Additional Questions?
Poster Presentation on Wednesday from 5-7 PM
Title: Remote Sensing-based Chlorophyll-a as a Proxy for Harmful Algal Bloom Public Health Advisories
Thank you!