## Slide 1: Aquaverse: An Aquatic Inversion scheme for remote sensing of fresh and coastal waters
Akash Ashapure1,2, Nima Pahlevan1,2, William Wainwright1,2, Brandon Smith1,2, Arun Saranathan1,2, Sakib Kabir1,2, Peng-Wang Zhai3
1 Science Systems and Applications Inc. (SSAI), Lanham, MD 20706, USA
2 NASA Goddard Space Flight Center, Greenbelt, MD 20771, USA
3 Physics Department, University of Maryland Baltimore County, Department of Physics, Baltimore, MD, 21250
Session: Existing, emerging, and future of remote sensing
05/09/2023
Ocean Biology and Biogeochemistry, the Carbon Cycle and Ecosystems workshop 2023 College Park MD

## Slide 2
Stressors
  Wildfire, flooding
  Food production, Mining….
Impacts
  Water pollution
  Harmful Algal Blooms
Consequence & implications
  Public health
  Economy
Introduction
Aquatic ecosystem are under threat!

## Slide 3
Optical satellite datasets are gaining popularity for environmental applications
Atmospheric correction is most challenging processing component
A large fraction of useable signal originates from scattering and absorption within the atmosphere
Introduction

## Slide 4
Lessons learned from ACIX-Aqua
Evaluated eight state-of-the-art atmospheric correction methods implemented on Landsat-8/OLI and Sentinel-2/MSI imagery
Pahlevan et al. 2021. ACIX-Aqua: A global assessment of atmospheric correction methods for Landsat-8 and Sentinel-2 over lakes, rivers, and coastal waters. Remote Sensing of Environment, 258, 112366
Coastal (AERONET-OC)
Inland
Median Accuracy [%]
Goal:
Develop an atmospheric correction processor that outperforms the state-of-the-art.
Target missions:
Landsat-8/OLI and Sentinel-2/MSI
MSI - Multispectral Imager
OLI - Operational Land Imager

## Slide 5
Use histogram matching to subset an in situ Rrs database
  Rrs (N~525) Rrs (N~11,000)
Simulate 𝜌t using a vector RT code (Zhai et al. 2009)
  Incorporate in situ Rrs (400 – 800)
  Solar Zenith, View Zenith, Azimuth
  # of Aerosol models: ~ 60 (Ahmad et al. 2010 + Montes et al. 2022)
  AOT(550): 0.01 – 0.7
  Water Vapor: Sub-arc winter, Mid-lat summer, Tropical
Network structure
Determine Globally Representative Rrs N ~ 525
Simulate TOA reflectance (𝜌t @5 nm)
Geometry
Aerosol Models
AOT
Water Vapor
Resample with MSI/OLI RSR
Inverse Model (𝜌t, 𝜽, 𝜽s ,Δ𝜙  Rrs)
Testing/Validation
AERONET-OC
Campaign Data
Model development: Mixture Density Networks

## Slide 6
Combined AERONET-OC and GLORIA data led to > 1100 OLI and MSI matchups
Matchup assessments
GLORIA & AERONET-OC
GLORIA dataset source: Lehman et al. 2023 GLORIA - A globally representative hyperspectral in situ dataset for optical sensing of water quality
https://doi.org/10.1038/s41597-023-01973-y

## Slide 7
Performance summary
AQUAVERSE OLI
AQUAVERSE MSI
AQUAVERSE OLI
AQUAVERSE MSI

## Slide 8
MSI (17/10/2020 16:02 GMT)
OLI (17/10/2020 15:45 GMT)
Visual assessment: Chesapeake Bay

## Slide 9
Visual assessment: Upper Klamath Lake
MSI (07/29/2019 19:02GMT)
OLI (07/29/2019 18:50GMT)

## Slide 10
Extend retrievals beyond 800 nm.
Improve the angular resolution of our training set.
Enhance the optical representation of our input spectra.
Evaluate downstream products.
Devise and integrate a robust cloud-masking approach.
Ongoing/future work

## Slide 11
Contact:
Akash Ashapure
Email: akash.ashapure@nasa.gov
Dr. Nima Pahlevan
Dr. Arun Saranathan
Mr. Brandon Smith
Mr. Sakib Kabir
Mr. William Wainwright
Dr. Peng-Wang Zhai
Acknowledgement
NASA Earth Science Programs
Ocean biology and Biogeochemistry
Remote sensing of water quality
United States Geological Survey
Landsat Science Team